Architetture dei Sistemi di Elaborazione	Delivery date: / October 25th 2023
Laboratory / 2	Expected delivery of lab_02.zip must include: / program_1.s and program_2.s / This file, filled with information and possibly compiled in a pdf format.

Please, configure the winMIPS64 simulator with the Base Configuration provided in the following (in italics not user controllable configuration):
- Code address bus: 12
- Data address bus: 10
- Pipelined FP arithmetic unit (latency): 3 stages
- Pipelined multiplier unit (latency): 8 stages
- divider unit (latency): not pipelined unit,
20 clock cycles
- Forwarding is enabled
- Branch prediction is disabled
- Branch delay slot is disabled
- Integer ALU: 1 clock cycle
- Data memory: 1 clock cycle
- Branch delay slot: 1 clock cycle.

Write an assembly program (program_1.s) for the winMIPS64 architecture described before able to implement the following piece of code described at high-level:
for (i = 0; i < 64; i++) {
v5[i] = ((v1[i]* v2[i]) + v3[i]) + v4[i];
v6[i] = v5[i]/(v4[i]+v1[i]);
v7[i] = v6[i]*(v2[i]+v3[i]);
}

Assume that the vectors v1[], v2[], v3[], and v4[] are allocated previously in memory and contain 64 double precision floating point values; assume also that v1[] and v4[] do not contain 0 values. Additionally, the vectors v5[], v6[], v7[] are empty vectors also allocated in memory.

Calculate the data memory footprint of your program:

Data	Number of Bytes
V1
V2
V3
V4
V5
V6
V7
Total

Are there any issues? Yes, where and why? No ? Do you need to change something?

Your answer:

ATTENTION: winMIPS64 has a limitation due to the underlying software.
There is a limitation in the string length when declaring a vector. Split the vectors elements in multiple lines (it also increases the readability) .

Example: my_fancy_vector: .byte 4, 5 ,7, 8
.byte 5,77, 8
.byte ……

    1. Compute the CPU performance equation (CPU time) of the previous program following the next directions, assume a clock frequency of 1MHz:
"CPU time" =(sum from {i = 1} to {n} <"CP" {"I"} rsub {i} × "I" {"C"} rsub {i} )× "Clock cycle" " " "period"

      1. Count manually, the number of the different instructions (ICi) executed in the program
      2. Assume that the CPIi for every type of instructions equals the number of clock cycles in the instruction EXE stage, for example:
        1. integer instructions CPI = 1
        2. LD/SD instructions CPI = 1
        3. FP MUL instructions CPI = 8
        4. FP DIV instructions CPI = 20
        5. …

    1. Compute by hand again the CPU performance equation assuming that you can improve the FP Multiplier or the FP Divider by speeding up by 2 only one of the units at a time:
      1. Pipelined FP multiplier unit (latency): 8  4 stages
Or
      1. FP Divider unit (latency): not pipelined unit, 20  10 clock cycles

Table 1: CPU time by hand
	CPU Time initial (a)	CPU Time / (b – MUL speed up)	CPU Time / (b – DIV speed up)
program_1.S

    1. Using the simulator calculate again the CPU time and complete the following table:

Table 2: CPU time using the simulator
	CPU Time initial (a)	CPU Time / (b – MUL speed up)	CPU Time / (b – DIV speed up)
program_1.S

Are there any difference? If yes, where and why? If Not, provide some comments in the following:

Your answer:

    1. Using the simulator and the Base Configuration, disable the Forwarding option and compute how many clock cycles the program takes to execute.

Table 3: forwarding disabled
	Number of clock cycles	IPC (Instructions Per Clock)
program_1.S

Enable one at a time the optimization features that were initially disabled and collect statistics to fill the following table (fill all required data in the table before exporting this file to pdf format to be delivered).

Table 4: Program performance for different processor configurations
Program	Forwarding		Branch Target Buffer		Delay Slot		Forwarding + Branch Target Buffer
	IPC	CC	IPC	CC	IPC	CC	IPC	CC
Program_1.S

Using the WinMIPS64 simulator, validate experimentally the Amdahl’s law, defined as follows:
size 12{"speedup" rSub { size 8{"overall"} } = { {"execution time" rSub { size 8{"old"} } } over {"execution time" rSub { size 8{"new"} } } } = { {1} over { \( 1 - "fraction" rSub { size 8{"enhanced"} } \) + { {"fraction" rSub { size 8{"enhanced"} } } over {"speedup" rSub { size 8{"enhanced"} } } } } } } {}

Using the program developed before: program_1.s

Modify the processor architectural parameters related with multicycle instructions (MenuConfigureArchitecture) in the following way:

        1. Configuration 1
          1. Starting from the Base Configuration, change only the FP addition latency to 6
        2. Configuration 2
          1. Starting from the Base Configuration, change only the Multiplier latency to 4
        3. Configuration 3
          1. Starting from the Base Configuration, change only the division latency to 10

Compute by hand (using the Amdahl’s Law) and using the simulator the speed-up for any one of the previous processor configurations. Compare the obtained results and complete the following table.

Table 5: program_1.s speed-up computed by hand and by simulation
Proc. Config. / Speed-up comp.	Base config. / [c.c.]	Config. 1	Config. 2	Config. 3
By hand
By simulation

Write an assembly program (program_2.s) for the winMIPS64 architecture able to compute the output (y) of a neural computation (see the Fig. below):

x = sum from {j =0} to {K -1} {{i} rsub {j} * {w} rsub {j} + b}
y = f(x)

      where, to prevent the propagation of NaN (Not a Number), the activation function f is defined as:

f left (x right ) = left lbrace stack { 0, &if the exponent part of x is equal to 0x7ff # x, &otherwise } right none

Assume the vectors i and w respectively store the inputs entering the neuron and the weights of the connections. They contain K=30 double precision floating point elements. Assume that b is a double precision floating point constant and is equal to 0xab, and y is a double precision floating point value stored in memory.
Compute y.

Below is reported the encoding of IEEE 754 double-precision binary floating-point format:

Given the Base Configuration, run your program and extract the following information.

	Number of clock cycles	IPC (Instructions Per Clock)	CPI (Clock per Instructions)
program_2.S