Considering the MIPS64 architecture presented in the following:
Integer ALU: 1 clock cycle / Data memory: 1 clock cycle / FP multiplier unit: pipelined 6 stages	FP arithmetic unit: pipelined 3 stages / FP divider unit: not pipelined unit that requires 6 clock cycles / branch delay slot: 1 clock cycle, and the branch delay slot disabled	forwarding enabled / it is possible to complete instruction EXE stage in an out-of-order fashion.

and using the following code fragment, show the timing of the presented loop-based program and compute how many cycles does this program take to execute?
for (i = 0; i < 100; i++) {
v7[i] = (v1[i]*v2[i]+v3[i]/v4[i]+v5[i]/v6[i]);
  }
.data					Clock cycles
V1: .double “100 values”
V2: .double “100 values”
V3: .double “100 values” / … / V5: .double “100 zeros”
V4: .double “100 values”
V5: .double “100 values”
V6: .double “100 values”
.text
main: daddui r1,r0,0	F	D	E	M	W					5
daddui r2,r0,100		F	D	E	M	W					1
loop: l.d f1,v1(r1)			F	D	E	M	W					1
l.d f2,v2(r1)				F	D	E	M	W					1
l.d f3,v3(r1)					F	D	E	M	W					1
l.d f4,v4(r1)					F	D	E	M	W					1
l.d f5,v5(r1)					F	D	E	M	W					1
l.d f6,v6(r1)					F	D	E	M	W					1
mul.d f7,f1,f2					F	D	X	X	X	X	X	X	M	W					6
div.d f8,f3,f4					F	D	d	d	d	d	d	d	M	W					1
div.d f9,f5,f6					F	D	s	s	s	s	s	d	d	d	d	d	d	M	W					6
add.d f10,f8,f7					F	s	s	s	s	s	D	A	A	A	M	W					0
add.d f10,f9,f10					F	D	s	s	s	s	A	A	A	M	W					3
s.d f10,v7(r1)					F	s	s	s	s	D	E	s	S	M	W					1
daddi r2,r2,-1					F	D	s	s	E	M	W					1
daddui r1,r1,8					F	s	s	D	E	M	W					1
bnez r2,loop					F	D	E	M	W					1
halt					F	-	-	-	-					1

Total					2506->2705

Considerando il programma precedente, lo si ottimizzi in modo da eliminare per quanto possibile gli stalli del programma usando le tecniche note come rescheduling e register renaming. Si calcoli il tempo di esecuzione del nuovo programma nella stessa architettura evidenziando il miglioramento ottenuto.
				Clock cycles

Total